## Slide 1
Personal Protective Equipment in the makerspace

## Slide 2
SBME Makerspace: Split By Function
The makerspace is split into 2 rooms, the additive and subtractive spaces.
Each room has its own equipment and therefore rules for PPE usage and safety considerations.
There will be specific safety and PPE training for each tool which requires it, this is meant as an overview.
REMEMBER: IF YOU HAVENT BEEN TRAINED ON A TOOL YET, ASK A TA OR THE TECH

## Slide 3
SBME Makerspace: Additive Hazards
The additive space is used mainly for electronics and 3D printing, but may also have miscellaneous equipment in the space at times.
The main safety considerations include:
    Handling of resin (and resin / IPA - contaminated materials)
    Electrical shock
    Cuts / lacerations
    Fumes from soldering

## Slide 4
SBME Makerspace: Additive Hazards
Resin and FDM printers:
    Always wear nitrile gloves when working with uncured or partially cured resin.
    Never touch the nozzle of the FDM printer during use (it operates at 200 Celsius!).
    Ensure overhead ventilation is on during printer usage.
    Do not adjust settings or perform filament changes without supervision or approval.
    If a printer is causing failures, notify a TA or the Technician.

## Slide 5
SBME Makerspace: Additive Hazards
The equipment and components used in the makerspace are generally low voltage and low current, but care must still be taken.
    Solder only under an active vent hood.
    Plug soldering irons into timed outlets.
    Do not use equipment with exposed or frayed wires / cords, especially if connecting a power supply or wall outlet.
    Do not work near water hazards or flammable materials.
    Do not disassemble electrical equipment.

## Slide 6
SBME Makerspace: Subtractive Hazards
The main hazards in the additive space to be aware of include:
    Lacerations and more severe physical injuries from power tools.
    Inhalants and fumes

## Slide 7
SBME Makerspace: Subtractive Hazards
PPE for the subtractive space includes safety glasses, face shields, nitrile gloves, work / cut resistant gloves, N95 masks, hearing protection and more for specific tasks.
All PPE can be found either by its associated piece of equipment or in the grey PPE cabinet.
While certain tools require different PPE, generally speaking…

## Slide 8
SBME Makerspace: Subtractive Hazards
All jewellery MUST be removed before entering the space.
Long hair (or headscarves and other headwear) tied back or secured.
Closed toed shoes MUST be worn.
Safety glasses MUST be worn at ALL times.
Use all guards present on equipment.
NEVER wear gloves or long loose sleeves with power tools.
DO wear gloves when working with manual blades or sharp materials.
Always unplug power tools while making adjustments or leaving the tool.